TMT laser requirements summary

| Performance parameters | Design limits |
| --- | --- |
| Laser power, W | >50 | Laser volume, m | <2.4x3.7x1.2 |
| Polarization | Circular | Electronics volume, m | <2.4x1.3x1.0 |
| Pulse format | CW or mode-locked CW | Total mass, kg | <2600 |
| Line width, GHz | <1.5 (goal 0.050) | Electrical power | <60A @ 208V |
| Beam quality, xDL | <1.1 (goal 1.0) | Other | Variable gravity vector |

LGS WFS signal estimate

| Variable | Definition | Value |
| --- | --- | --- |
| Npde | Photodetection events per subaperture per frame | To be computed |
| A | WFS subaperture area, m2 | 0.25 or 0.0625 |
| Cs | Column density, sodium ions/m2 | 3×1013 |
| PL | Average laser power, W | Variable |
| S | Unsaturated coupling efficiency, photons-m2-s-W/ion | 260 |
| TAOS | End-to-end AO system efficiency, photoelectrons/photon | 0.45 (NFIRAOS estimate including telescope optics, AO system optics, and WFS detector QE) |
| TATM | One-way atmospheric transmittance at zenith | 0.80 |
| TLSGF | End-to-end LGSF transmittance | 0.75 (includes beam transfer optics and launch telescope) |
|  | WFS integration time, sec | 0.00125 (800 Hz frame rate) |
|  | Zenith angle, degrees | 0 |
| Z | Sodium layer range, m | 90×103 |